## Slide 1: Descriptive and inferential statistical methodologies have proven effective in creating a proactive ‘alarm’, accurately identifying Pump Failures with Horse Power (HP) and Pump Efficiency (PE) emerging as key variables of interest with deviations of 15 HP and > 3 % PE being our core signal thresholds.
Chart: Correlation Coefficient Pump Failure (Rolling StDev 30 Minute)
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
 | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726
Chart: Statistical Alarm Plot

## Slide 2: Descriptive Analysis has enabled us to clearly identify particular signature abnormalities showing clear signature changes in both Rolling Standard Deviation and Rolling Mean Datasets when observed over the respective failure period of interest.
Chart: Rolling Mean 30M Time Series Plot
Chart: Rolling Standard Deviation 30M Time Series Plot

## Slide 3: Further segmentation of the data via binary means (Pump Failure = 0 or 1) illustrated through box plots, show a clear signature difference between that of normal behaviour and that of Failure with Pump Torque, Pump Speed, and Ambient Temperature showing the 3 largest variances.

## Slide 4: Correlation analyses across datasets yield interesting insights with Pump Efficiency (-0.62) and Volumetric Flow Meter (-0.62) negatively correlated with Pump Failure in the Rolling Mean Data, whilst Horse Power (0.69) and Volumetric Flow Meter 1 (0.64) show a subsequently strong positive in the Rolling Stdev Dataset.
Chart: Correlation Coefficient Associated with Pump Failure (Raw Data)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
Correlation Coefficient | 0.42184 | 0.26001 | 0.23318 | 0.20801 | -0.10249 | -0.10268 | -0.11211
Chart: Correlation Coefficient Associated with Pump Failure (Rolling Mean)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
 | 0.44799 | -0.098164 | -0.13299 | -0.19744 | -0.61654 | -0.61721 | -0.62067
Chart: Correlation Coefficient Associated with Pump Failure (Rolling StDev)
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
 | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726

## Slide 5: Lastly, analysis of the model fit reveals that with a R Squared of 0.78, a linear model is a good fit for the data with variables Horse Power, Pump Efficiency and Volumetric Flow Meter 2 having the largest coefficients, indicative that these variables have the most immediate relationship with respect to Pump Failure behaviour.
Chart: Variable Regression Coefficients
| Horse Power | Pump Efficiency | Volumetric Flow Meter 1 | Ambient Temperature | Pump Speed (RPM) | Pump Torque | Volumetric Flow Meter 2
 | 0.76485 | 0.34237 | 0.050934 | 0.018207 | -0.017867 | -0.018902 | -0.61136